## Slide 1: VM Simulation with EPICS PV Naming VM Version Control and Network

## Slide 2
Noise and ramping current have been added to the simulation of the virtual magnets.
Noise is adjustable. Here it is about 5%
VM PV example:BSOL at 5A with noise
Time
Amps
We can currently simulate VELA:
Magnets  Polarity and interlocks
Camera
Screens
BPM
User PVs

## Slide 3
EPICS provides a common control interface and interlocks between the hardware and the user. Its communication layer is via Process Variables (PVs). The user can set and read to these PVs
For ALICE and VELA there are hundreds of PVs. Only a handful of these are useful to the end user. These were named “organically”
For CLARA/VELA there is an effort to developing a consistent naming model for the PVs
Developing the VM has spawned a collaboration between the AP and controls group and that is useful for this goal
PV naming

## Slide 4
It is important that the VM names do not clash with the real machine or other users machines. However EPICS IOCs makes pervasive use of the network connection to communicate with clients. We do not want problems with rouge IOCs in the future if the VM becomes prevalent. This could affect IOCs operating on the real machine
Allowing the VM onto the internet would allow parallel Astra simulations and the use of a Git repository for updates
With an upgrade to the EPICE version it is be possible to contain EPICS to the users machine and avoid these PV naming conflicts
Also, tag “VM_” has been added to the controls document for virtual PVs so their should be no conflicts with real PVs
Version control and network